## Slide 1
$ free -h
Swap: 4.0Gi 0B 4.0Gi
$ _
RED HAT ENTERPRISE LINUX
Understanding & Creating
Swap Space
A practical guide to virtual memory, swap files, swap partitions, and disk-based swap management in RHEL
10 SLIDES · SYSTEM ADMINISTRATION

## Slide 2
What Is Swap Space?
A reserved area of disk that extends your system's usable memory
i
Definition
Swap space is disk storage used by the Linux kernel as an overflow for RAM.
When physical memory (RAM) fills up, inactive pages are moved to swap, freeing RAM for active processes.
It is slower than RAM but prevents applications from crashing due to out-of-memory errors.
RAM
Fast
Volatile — cleared on reboot
SWAP
Slower
Persistent on disk until removed
Where it lives
A dedicated swap partition, or
A swap file on an existing filesystem
RHEL Swap Space
2

## Slide 3
Why Swap Space Is Needed
Four reasons swap remains a standard part of RHEL system design
⚠
Prevents OOM crashes
Gives the kernel room to move idle pages out of RAM instead of killing processes when memory runs low.
⏸
Supports hibernation
Suspend-to-disk writes the entire RAM image into swap so the system can resume later.
➕
Extends effective memory
Lets a system handle memory spikes beyond installed RAM, useful on smaller VMs and servers.
⚙
Improves stability under load
The kernel can proactively swap out rarely used pages, keeping more RAM free for disk cache.
RHEL Swap Space
3

## Slide 4
Two Ways to Configure Swap
RHEL supports swap on a dedicated partition or inside a regular file
≡
Swap Partition
A dedicated disk partition (type Linux swap) used exclusively for swap.
PROS
Slightly faster; simple, predictable performance; standard on physical servers.
CONS
Fixed size; resizing requires repartitioning or LVM.
▤
Swap File
A regular file on an existing filesystem, formatted and enabled as swap.
PROS
Easy to create, resize, or remove without touching partitions. Great for VMs and cloud instances.
CONS
Marginally slower on some filesystems (not on XFS/ext4 with proper setup).
RHEL Swap Space
4

## Slide 5
Check Current Swap Status
Always confirm what's already configured before adding more swap
# View swap usage summary
$ free -h
# List active swap devices
$ swapon --show
# Detailed memory + swap info
$ cat /proc/swaps
# Check block devices & sizes
$ lsblk
What to look for
Total vs. Used
"free -h" shows how much swap exists and how much is in use right now.
Active devices
"swapon --show" lists every partition or file currently acting as swap, with type and priority.
Free disk space
Confirm there's enough free space on the target filesystem before creating a swap file.
Existing partitions
"lsblk" reveals unpartitioned or unused space that could become a swap partition.
RHEL Swap Space
5

## Slide 6
Create a Swap File — Step by Step
The most flexible way to add swap on RHEL
1
Allocate the file
sudo fallocate -l 2G /swapfile
Reserves 2 GB. If fallocate isn't supported by the filesystem, use dd instead.
2
Secure the permissions
sudo chmod 600 /swapfile
Only root should be able to read or write the swap file.
3
Format as swap
sudo mkswap /swapfile
Writes a swap signature so the kernel recognizes the file.
4
Enable it
sudo swapon /swapfile
Activates the swap file immediately for the current session.
RHEL Swap Space
6

## Slide 7
Create a Swap Partition
Use a dedicated partition when you need consistent, predictable performance
# 1. Create the partition (interactive)
$ sudo fdisk /dev/sdb
Command (m for help): n -> new partition
Command (m for help): t -> change type
Hex code: 82 -> Linux swap
Command (m for help): w -> write & exit
# 2. Format the partition as swap
$ sudo mkswap /dev/sdb1
# 3. Activate it
$ sudo swapon /dev/sdb1
✓
Good to know
Use a blank or unused disk/partition — this process is destructive to existing data.
On GPT disks, parted can be used instead of fdisk with type code 8200.
LVM logical volumes can also be formatted as swap the same way with mkswap.
RHEL Swap Space
7

## Slide 8
Make Swap Permanent
swapon activates swap only until reboot — /etc/fstab makes it stick
# Back up fstab first
$ sudo cp /etc/fstab /etc/fstab.bak
# Append the swap entry
$ echo '/swapfile none swap sw 0 0' \
| sudo tee -a /etc/fstab
For a partition, use its UUID instead of a path:
UUID=xxxxxxxx-xxxx none swap sw 0 0
Find it with: blkid /dev/sdb1
↻
fstab fields, explained
Device
Path or UUID of the swap file/partition
none
Swap has no mount point
swap
Filesystem type
sw
Mount option for swap
0 0
Dump and fsck order — always 0 for swap
Test it without rebooting:
sudo mount -a && sudo swapon -a
RHEL Swap Space
8

## Slide 9
Managing & Tuning Swap
Common day-two operations once swap is up and running
✖
Disable a swap file/partition
sudo swapoff /swapfile
Deactivates swap; do this before deleting it.
🗑
Remove a swap file
sudo rm /swapfile
Also delete its line from /etc/fstab.
⚖
Check swappiness
cat /proc/sys/vm/swappiness
0-100 scale; controls how aggressively the kernel swaps (default 60).
✎
Adjust swappiness
sudo sysctl vm.swappiness=10
Lower values favor RAM; set permanently in /etc/sysctl.conf.
RHEL Swap Space
9

## Slide 10
Best Practices & Recap
Sizing guidance and the key takeaways from this deck
Recommended Swap Sizing (RHEL guidance)
≤ 2 GB RAM
2x RAM
2-8 GB RAM
Equal to RAM
8-64 GB RAM
0.5x RAM
> 64 GB RAM
4-8 GB (or per workload)
Hibernation systems need swap ≥ total RAM, regardless of the table above.
Key Takeaways
✓
Swap extends RAM using disk — slower, but prevents OOM crashes
✓
Choose a swap file for flexibility, a partition for raw performance
✓
mkswap formats, swapon activates, /etc/fstab makes it permanent
✓
Verify with free -h and swapon --show after every change
✓
Size swap to workload — more isn't always better
RHEL Swap Space
10